## Slide 1: Multibeam Advisory Committee RVTEC Update - 5 Nov 2025 - La Jolla, CA Paul Johnson, Vicki Ferrini, Kevin Jerram www.mac.unols.org mac-help@unols.org
Supported by NSF grants 1933720 (UNH) 1933776 (LDEO)

## Slide 2: MAC Updates

## Slide 3: The Multibeam Advisory Committee (MAC)
Established in 2011 with NSF funding to support collection of high-quality multibeam data across the U.S. Academic Research Fleet (USARF)
Standardized system testing workflows
  Sea Acceptance, Quality Assurance, Noise
On-board & remote support
  Flexible scheduling by ship request
Public reporting
  Technical reports and resources
  Assessment tools, survey guidance
  Non-USARF references
Website: mac.unols.org
Helpdesk: mac-help@unols.org
Wiki: oceanmapping.wiki
Notes: Since 2011 MAC has worked to improve MB data quality
Standardize performance testing
Provide on-board and remote support
Report all major testing activities
Website, helpdesk, wiki

## Slide 4: Multibeam Systems Supported by the MAC
12 Vessels with MBES
  10 UNOLS Research Vessels
  2 Icebreakers
15 Deep water systems
  EM122 / EM124 (12 kHz)
  EM304 MKII (26-34 kHz)
  EM710 / EM712 (40-100 kHz)
2 Shallow water systems
  EM2040 (200-400 kHz)
+7 Systems in 2026+
  EM304s & EM2040s (RCRVs)
  EM2042 (SKQ)

## Slide 5: System Performance Testing
Planning
Review of recent data, issues, etc.
Vessel + sensor offset survey (as needed)
Site selection + scheduling
Software + firmware updates
Early as possible
Dockside
1-2 days
At Sea
1-10 days
Configuration + offset review
Hardware health check
Test plan review with bridge (ongoing)
GNSS antenna calibration
Multibeam calibration (‘patch test’)
RX noise vs. speed / seas
Swath coverage (extinction)
Swath accuracy
Water column evaluation
Backscatter normalization
Data and configuration backup
Public reporting (MAC website)
Opportunistic testing
Follow-Up
1-2 mos.
Notes: Follow a standard order of operations
Applies for ON BOARD and REMOTE support
Takeaway: support is by request, early as possible

## Slide 6: Kongsberg Installations and Life Cycles
Italic = pending replacement (2026+)
Green = testing in last year
ANT = Acoustic Noise Test (Gates)
Ship | System(s) | Arrays | Life Cycle | MAC Support (Most Recent) | 2025-26 Plans
Atlantis | EM124 (g) | 2021 | Early | SAT*, QAT (2024) | QAT
Healy | EM122 | 2010 / 2023 RX | Late | ANT, SAT*, QAT* (2025) | QAT
Hugh R. Sharp | EM2040 | 2024 | Early | QAT (2016), SAT (Kongsberg) | EM2040 SAT
Kilo Moana | EM122 / EM710 | 2012 | Late | ANT, QAT* (2023), spares planning | QAT
Marcus G. Langseth | EM122 (g) | 2007 TX / 2010 RX | Late | ANT, QAT (2023), spares planning | QAT
Nathaniel B. Palmer | EM122 | 2015 | Late | SAT, ANT, QAT (2015), spares planning | TBD
Neil Armstrong | EM124 / EM712 | 2024 (2016 710 RX) | Early | SAT* (2024) | QAT
Rachel Carson | EM2040 | 2024 | Early | SAT* (2024) | QAT
Roger Revelle | EM124 / EM712 (g) | 2020 | Mid | SAT*, QAT* (2025) | QAT
Sikuliaq | EM304 MKII / EM710 | 2024 | Early/Late | SAT, QAT (2025) | EM2042 SAT
Sally Ride | EM124 / EM712 | 2016 | Mid | SAT, QAT (2025) | QAT
Thomas G. Thompson | EM124 (g) | 2025 | Mid | SAT, QAT*, EM124 SAT planning | EM124 SAT
(g) indicates gondola installation
*Indicates remote support
Underline = recent install

## Slide 7: Recent Takeaways
MAC approaches reinforce manufacturer protocols
Offset survey requirements are critical
  Linear offsets on order of 0.001 m
  Angular offsets on order of 0.01°
  Clear reporting for direct configuration
Standard calibration procedures are efficient
  Standardized + quantitative ≈ repeatable
  Specific seafloor types for each test
Configurations are managed by system owners
  Users may apply different offsets in post-proc

## Slide 8: Related Activities Since RVTEC 2024
MAC-related projects:
Ocean Mapping Community Wiki
Echosounder Test Site Database
Sound Speed Manager
GMRT tiling package
Assessment tools
Spares planning
Survey support
Non-MAC field work:
David Packard (SAT)
Nautilus (QAT)
OceanXplorer (QAT)
Oden (SAT)
DriX O-16 (SAT)
Notes: Quick highlights since 2024
MAC-related projects
Other field work that improves the process

## Slide 9: Vessel Offset Survey Support
Focus Area | Key Action
Verification | Verification surveys and cross-checks
Quality Assurance | On-site consultancy and survey supervision
Review | Evaluation / feedback for improving survey accuracies
Standards | Drafting of survey specifications and requirements
Coordination | Communication with survey contractors
R/V Thomas G Thompson
Sep 2025: On-site survey technical consultancy and verification survey
R/V Roger Revelle
March 2025: Verification survey

## Slide 10: The (Next) Multibeam Advisory Committee (MAC)
Current grant is ending mid-2026
Next proposal will include:
Continuing on-board and remote support
Continuing helpdesk email support
Expansion of planning and assessment tools
Support for vessel / sensor offset surveys
  Technical guidance and review
  Not replacing commercial surveyors
Your feedback and suggestions
  What do you need from the MAC?
Notes: Since 2011 MAC has worked to improve MB data quality
Standardize performance testing
Provide on-board and remote support
Report all major testing activities
Website, helpdesk, wiki

## Slide 11: Ocean Mapping Community Wiki

## Slide 12: Ocean Mapping Community Wiki
oceanmapping.wiki
omcadmin@ccom.unh.edu
Notes: MAC continues to use the OMC Wiki
Co-admins with Shannon Hoy and Colleen Peters
Public platform to share resources and post issues
Sticking with Github for now

## Slide 13: Ocean Mapping Community Wiki
oceanmapping.wiki
omcadmin@ccom.unh.edu
Notes: Like all wikis, this grows from the user base
All are welcome to contribute
Post ISSUES or add areas of interest
Lots of resources for new members
Email Wiki or MAC helpdesk for more

## Slide 14: Ocean Mapping Community Wiki
oceanmapping.wiki
omcadmin@ccom.unh.edu

## Slide 15: Assessment Tools

## Slide 16: Assessment Tools: BIST Plotter

## Slide 17: Assessment Tools: BIST Plotter

## Slide 18: Assessment Tools: Swath Accuracy Plotter

## Slide 19: Assessment Tools: Swath Accuracy Plotter

## Slide 20: Assessment Tools: Swath Coverage Plotter

## Slide 21: Assessment Tools: Swath Coverage Plotter

## Slide 22: Assessment Tools: Swath Coverage Graph Digitizer
Digitize theoretical swath
coverage for comparison

## Slide 23: Planning Tools: GMRT Downloader

## Slide 24: Planning Tools: SAT/QAT Planner

## Slide 25: Other Tools: ECDIS Converter and File Trimmer

## Slide 26: Test Site Database

## Slide 27: Test Site Database
https://gis.ccom.unh.edu
Notes: Reuse proven test sites whenever possible
Building a web interface to simplify this process
Interface includes several planning layers
Each site includes line plans, settings, reports
Backlog of MAC sites to be added

## Slide 28: Test Site Database
https://gis.ccom.unh.edu

## Slide 29: Test Site Database
https://gis.ccom.unh.edu

## Slide 30: Test Site Database
https://gis.ccom.unh.edu

## Slide 31: Test Site Submission Form
https://forms.gle/5EdGwomMF116DprFA

## Slide 32: R2R, MGDS, GMRT

## Slide 34: Transit Mapping

## Slide 35: Sound Speed Manager

## Slide 36: Sound Speed Manager
A ready-to-go and free
solution to ease
the management of
sound speed profiles
for ocean mapping
Ref.: Masetti, G. et al., Sound Speed Manager: An open-source application to manage sound speed profiles, International Hydrographic Review, vol. 17, pp. 31-40, 2017.
https://www.hydroffice.org/soundspeed/
POCs: Giuseppe (gmasetti@ccom.unh.edu),
Barry (barry.gallagher@noaa.gov),
Chen (chen.zhang@noaa.gov)
https://svn.pydro.noaa.gov/Docs/html/Pydro/downloads.html

## Slide 37: Sound Speed Manager
10k+
2016 →
Jointly developed by CCOM/JHC & NOAA OCS
Notes: We started the merge, and at the beginning of 2016 the first release of Sound Speed Manager was made publicly available.
Since then, we have been developing and improving Sound Speed Manager.
SSM has now reached a good level of maturity, with an important users base spanning from the scientific community to several commercial companies. It is widely used both within the US and world-wide with more than 10,000 downloads just from the HydrOffice website.

## Slide 38: Recent Updates
  NMEA-0183 network listener
  Recent Ops Forecast Systems
  Metadata and stats customization
New Features
  #SSM datagram & user guide
  Interaction status on taskbar
Better SIS & HYPACK Integration
  AML, ASVP, CSV, NCEI, Valeport, etc.
Improved Supported Formats
Notes: For example, the addition of a generic NMEA-0183 network listener is a great example of contributed code that improves and extends Sound Speed Manager.
In this specific case, most of the credits for the contribution go to Jean-Guy Nistad from the German Hydrographic Office.

## Slide 39: Recent Updates
  NMEA-0183 network listener
  Recent Ops Forecast Systems
  Metadata and stats customization
New Features
  #SSM datagram & user guide
  Interaction status on taskbar
Better SIS & HYPACK Integration
  AML, ASVP, CSV, NCEI, Valeport, etc.
Improved Supported Formats
Notes: Recent changes to the NCEI Operational Forecast System have required relevant changes to continue the support for synthetic profiles derived from OFS.
During such a work, the support has been extended to recently added OFS like, for instance, the West Coast OFS.

## Slide 40: Recent Updates
  NMEA-0183 network listener
  Recent Ops Forecast Systems
  Metadata and stats customization
New Features
  #SSM datagram & user guide
  Interaction status on taskbar
Better SIS & HYPACK Integration
  AML, ASVP, CSV, NCEI, Valeport, etc.
Improved Supported Formats
DataDistrib bug in SIS 5.15.0!
Notes: Relevant improvements have been applied to the integration with Hypack and Kongsberg Sis.
The ongoing collaboration with Kongsberg has triggered the creation of a dedicated SSM datagram starting with Sis 5.14 (released in November 2024). This improvement greatly reduces the network traffic and further simplifies the SSM initial setup on the Sis app to a single field.
Furthermore, a guide to integrating SSM with Sis is now included in the Sis installation documentation.
Given the current bug for DataDistrib in SIS 5.15.0, using the #SSM datagram is the ONLY working method.

## Slide 41: Recent Updates
  NMEA-0183 network listener
  Recent Ops Forecast Systems
  Metadata and stats customization
New Features
  #SSM datagram & user guide
  Interaction status on taskbar
Better SIS & HYPACK Integration
  AML, ASVP, CSV, NCEI, Valeport, etc.
Improved Supported Formats
Notes: Another relevant improvement has been that the SSM taskbar now shows different colors to capture user attention in case of issues (for example, ‘Not pinging for a while’ alert).

## Slide 42: Recent Updates
  NMEA-0183 network listener
  Recent Ops Forecast Systems
  Metadata and stats customization
New Features
  #SSM datagram & user guide
  Interaction status on taskbar
Better SIS & HYPACK Integration
  AML, ASVP, CSV, NCEI, Valeport, etc.
Improved Supported Formats
Notes: Finally, the set of currently supported profile formats has been extended and improved.
The "Kongsberg driver" has been extended to not only export ASVP format, but also export SSP format (that also contains temperature and salinity). As also recently clarified in Sis documentation, the use of the SSP file ensures that all absorption coefficients are updated in Sis.
Furthermore, a few changes have been required during the year to extend and improve supported formats (for example, MiniCTD probes in the Valeport driver).

## Slide 43
Let’s keep building, together!
Visit: https://www.hydroffice.org/soundspeed/
Contact us at soundspeed@hydroffice.org
Notes: Finally, the set of currently supported profile formats has been extended and improved.
The "Kongsberg driver" has been extended to not only export ASVP format, but also export SSP format (that also contains temperature and salinity). As also recently clarified in Sis documentation, the use of the SSP file ensures that all absorption coefficients are updated in Sis.
Furthermore, a few changes have been required during the year to extend and improve supported formats (for example, MiniCTD probes in the Valeport driver).

## Slide 44: Questions? Answers? Reach out!
Multibeam Advisory Committee
https://mac.unols.org
mac-help@unols.org
Ocean Mapping Community Wiki
https://oceanmapping.wiki
omcadmin@ccom.unh.edu