## Slide 1: NSF Wire Pool
Eric Trotto

## Slide 2: What is the Wire Pool
The Wire Pool supports the tension members needs of the U.S. Academic Research Fleet
    Maintaining an inventory
    Coordinating requests
    Conducting break tests
    Maintaining a wire database

## Slide 3: Maintain An Inventory of Wire Rope, Cable, and Synthetic
One Wire Pool, two storage facilities
East Coast - Woods Hole Oceanographic Institution (WHOI)
West Coast - Scripps Institution of Oceanography (SIO)
Inventory of commonly used tension members
3x19 Wire Ropes: ¼”, ½”, 9/16”
Cables: .322” EM, .680” Coax, .681” power optic
Other tension members
Synthetics: 9/16” Plasma HiCo

## Slide 4: Requesting New Wire
Wire Pool fields all requests for new and used tension members
Determine availability of requested item (inventory)
Wire Pool prepares package for NSF consideration
If approved, arrange for shipping to nearest domestic port
Long Lead Times
.681”: 8 Month lead time
3x19: 4 Month lead time

## Slide 5: Break Testing
  Barbara Callahan, Wire Testing Coordinator
  Submit break test request via the Wire Pool database
    Testing mandated by Appendix A of RVSS and funded by NSF (no cost to vessel)
  Evaluate
  Recommendations

## Slide 6: Wire Pool Database
Andrea Harvey, Wire Pool Database Administrator
Manage wire and cable assigned to your Institution’s vessel(s)
    Update wire status (e.g. ‘In use’ or ‘Stored’)
    Manage Safe Working Load (SWL) information for cable and wire in use or onboard a vessel
    Report events (lubrication, cutback/re-termination, splits, end-for-end, document uploads)
    Submit break test requests and view results/recommendations
    Other Features
    Request wire or cable from the Wire Pool
    Add a tension member to a vessel (report a reel)
    Break test request
    Disposal request
    Add new users (full access or read-only)
    User-centric

## Slide 7: How are your terminations holding up?
  3x19 Wire rope
  Most comely used termination is NICO press
  What we see wrong?
  Improper dies and spacing
  Pressing in incorrect order
  Wrong thimble

## Slide 8: 3x19 Nico Pressed wire
Chart: 1/4”
Tested Breaking Load (lbs) | 7228 | 6503 | 8460 | 8810 | 8380 | 7290 | 6050 | 6538 | 7570 | 6600 | 7358 | 8283 | 6840 | 7576 | 7416 | 6637 | 6581 | 6839 | 7761 | 7398 | 6724 | 7710 | 7181 | 4925 | 7800 | 5993 | 6300 | 6375 | 7045 | 6320 | 7500
Chart: 9/16”
| 1 | 2 | 4 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 28 | 29 | 30 | 31
 | 28170 | 30630 | 31425 | 30400 | 27770 | 31900 | 32800 | 33920 | 33280 | 33200 | 31700 | 34925 | 30425 | 28010 | 22380 | 29600 | 31300 | 31870 | 33900 | 27500 | 29720 | 33325 | 27700 | 31950

## Slide 9: .322 Poured Socket
Chart: .322
 | 8405 | 9900 | 9650 | 11610 | 12000 | 13010 | 10550 | 11150 | 11660 | 12190 | 12510 | 11510 | 9098 | 9342 | 12650 | 11780 | 9810 | 12210 | 12490

## Slide 10: Mechanical
Chart: 9/16”
| 3 | 5 | 23 | 24 | 25 | 26
 | 31190 | 33150 | 31330 | 33040 | 34690 | 33090
Chart: .681
Tested Breaking Load (lbs) | 31240
Chart: .322
Tested Breaking Load (lbs) | 11110 | 10650 | 9020

## Slide 11: Helical Termination
Chart: .680”
| 1 | 2 | 3 | 4 | 6
Tested Breaking Load (lbs) | 28800 | 40220 | 27070 | 16510 | 30350
Chart: .681”
| 2 | 3
Tested Breaking Load (lbs) | 42420 | 15620
Chart: .322”
 | 10500 | 9300 | 10280 | 11480 | 9800 | 9730 | 10350 | 9350 | 7884 | 9600 | 8891 | 9353 | 10280 | 9064 | 10090 | 8824 | 8683 | 9449 | 8657 | 7887 | 7725 | 8959 | 11050

## Slide 12: Spooler
Hawboldt Industries spooler capable of spooling 10,000 M reels of .681
  Allows the Wire Pool to inspect and lubricate factory reels
  Cut from factory reels to distribute to vessels, saving on shipping costs

## Slide 13: Questions?