## Slide 1: Recent Advances in Underwater Robots at the Deep Submergence Laboratory James C. Kinsey1, Andrew D. Bowen1, Christopher R. German1, Michael V. Jakuba1, Carl L. Kaiser1, Larry Mayer,1,2, Adam S. Soule1, Louis L. Whitcomb1,3 and Dana R. Yoerger1 1Woods Hole Oceanographic Institution, 2University of New Hampshire, Center for Coastal and Ocean Mapping, 3The Johns Hopkins University

## Slide 2
Deep Submergence Lab
Design, build and operate a variety of ocean robots
Home to the National Deep Submergence Facility (NDSF)
Field Operations:
  10+ ROV cruises/year
  ~10 AUV cruises/year
Core areas include:
  Robotics
  Control and navigation
  Sensing
  Autonomy

## Slide 3
Deep Submergence Lab
Design, build and operate a variety of ocean robots
Home to the National Deep Submergence Facility (NDSF)
Field Operations:
  10+ ROV cruises/year
  ~10 AUV cruises/year
Core areas include:
  Robotics
  Control and navigation
  Sensing
  Autonomy
Today’s talk focuses on 2 recent projects:
  Coordinated AUV-ASV operations
  Nereid Under-Ice robot

## Slide 4
Coordinated AUV-ASV Operations
AUV Operations: Then
Credit: D. Yoerger WHOI
Use to deploy a deep AUV and leave it for 20+ hours to go do other work
LBL provided external nav aiding
Very minimal telemetry

## Slide 5
Strongest Plume Signal
Coordinated AUV-ASV Operations
AUV Operations Now:
Limited Acoustic Telemetry
Transmitted science data enabled interrogation of mission progress
Facilitated in-situ re-tasking of vehicle
Acoustic telemetry has transformed AUV operations however it has created an “acoustic leash” for many AUVs!
[Camilli et al. Science 2010]
[German et al. PNAS 2010]

## Slide 6
Joint operations with AUVs and ROVs or manned submersibles are increasingly common
For example, in the last year the Sentry AUV did 6 cruises with either the Jason ROV or the Alvin manned submersible
  With Alvin, Sentry dives at night for a 10-12 hour dive. Is recovered with a 50% battery charge.
  With Jason, Sentry operates within ~5km of the ship.
    Launch and recover with Jason in the water.
Efficiency could be improved if Sentry could operate far away from the ship without having to sacrifice:
  External navigation aiding
  In-situ monitoring and intervention
Joint Vehicle Operations
Image Credits: WHOI.

## Slide 7
CONOPS
  Actuated AUV and Waveglider
  AUV/ASV deployed and recovered from ship
  AUV performs mission as usual
  ASV, with knowledge of AUV mission plan, “tends” AUV
ASV as navigation aid
  Eliminates ship-required USBL systems or pre-deployed transponders
ASV as force-multiplier:
  Provides operators with real-time data and re-tasking capability
  Frees ship to perform other over-the-side operations
Autonomous AUV Tending

## Slide 8
Pilot Project Overview
PROJECT GOALS
Demonstrate basic feasibility in shallow water
  Wave-Glider ASV
  Iver2 AUV
Develop software that coordinates ASV trajectory with the AUV
Investigate performance of different WaveGlider ASV trajectories
  Comms and Nav constraints
Field tests
.

## Slide 9
Acoustic Cycle (WHOI Micro-modems)
Ping
Ping
Reply
WG GPS
& Range
Iver
State
State Estimate & Science Data
Iver State
GPS & Range
OWTT
Coordinator software on Wave-Glider manages acoustic communications cycle and determines ASV trajectory.
Navigation code uses DVL, compass, and range data to estimate AUV position.
WG GPS & Range for single-range nav
Notes: WHOI ,icro-modems (Lee Freitag)

## Slide 10
Oct 2012 Buzzards Bay Experiments - Results
AUV mission planned a-priori; ASV has knowledge of the mission.
ASV plans its trajectory based on the AUV trajectory and the current AUV position
External aiding provided by single acoustic modem ranges
Experiment demonstrated the following capabilities:
  Active control of the WG-ASV
  External navigation aiding using WG
  Using WG as a telemetry relay for data uplink and retasking

## Slide 11
Our long term vision for ASV-AUV deep ocean operations
AUV Tending
(10s of km)
Ridge-Segment
(100s of km)
Basin-Scale
(1000s of km)

## Slide 12: Nereid Under-Ice (NUI)
Nereid Under-Ice (NUI) focuses on exploring biological and physical environments in the polar regions including:
  Operations under fixed ice shelves
  Operations moving sea ice
Tasks include:
  Near-ice inspection and mapping
  Instrument emplacement
  Sediment sampling
  Grounding line inspection
Notes: PO and geo questions driven by climate change and sea-level rise questions.
Still don’t know much about biology. No known climate change importance.

## Slide 13: NUI Specifications

## Slide 14: NUI Concept of Operations: Light Fiber-Optic Tether Operations
Light-weight Armored Cable (10 m - 100 m)
Depressor (~50 kg)
Two-body launch :
No descent/ascent weights---Pilot has control.
Short descent (10-20 m)
Light-weight depressor/tow-body system, ~85kg, 2 m tall
nUI
Light Fiber-Optic Tether (20 km)
Tow-body (~35 kg)
Umbilical (5 m)
Operating Envelope
Acoustics package

## Slide 15: Equipment Overview: Over-the-side
nUI
1800 kg
1.8 m x 1.8 m x 3 m
Soft-line recovery
Transponders (2)
Benthos XT 6001
Deployed fore and aft
Battery powered
Depressor
(prototype)
~100 kg
2 m tall
Tow-Body
35 kg
1 m long
Mated to depressor for launch
≥ 5 m umbilical to nUI
Acoustics
Package
1000 m max depth
2 m tall
~40 kg

## Slide 16: NUI Summer 2014 Deployments at 83° N 6° W F/V Polarstern PS86

## Slide 17: Launch and Recovery

## Slide 18: Under-Ice

## Slide 19: Questions
jkinsey@whoi.edu