## Slide 1: How to Use Autonomous Underwater Vehicle Gliders to Make Your Oceanography Better
Autonomous Underwater Gliders
Describe some useful glider operations
  Endurance
  Footprint
  Weather
Kipp Shearman
College of Oceanic & Atmospheric Sciences
Oregon State University
Thanks to: RV Elakha Captain and Crew (OSU), J. Brodersen (OSU), Laura Rubiano-Gomez (OSU), C. Jones (WRC), F. Stahr (UW), Miss Linda Captain and Crew, T. Peery (OSU), F. Chan, K. Page-Albins (PISCO), Oscar Pizarro (UdeC), Gadiel Alarcon and Nadin Ramirez (UdeC)
Jack Barth
Anatoli Erofeev
Zen Kurokawa
Kate Adams
Piero Mazzini
Chris Ordoñez
Gonzalo Saldias
Alejandra Sanchez
OSU Glider Group:

## Slide 2: What’s a glider?
Autonomous underwater vehicle – a robot!
Flies by changing its buoyancy
  takes on water, becomes heavy and sinks
  wings turn vertical motion into forward motion
  expels water, becomes light and rises
  flies saw tooth pattern through the ocean
Slow, but can stay out a long time
  ½ knot
  3-4 week endurance
Collects same data you would on a research vessel at a fraction of the cost
  Research vessel: approx. $20K/day (fuel + crew)
  Glider: $150K to buy + $200-1000/day (batteries + communications + techs)
  3500 days of glider operation:
  3500 days x $20K/day – 4 x ($150K+3500 days x $1000/day) = $55 million saved!

## Slide 3
CTD
Optical Sensors (Chl, CDOM and Backscatter)
Pitch Batteries
Science Bay
Displacement Pump
Glider Control and more batteries
Air bladder
Aanderaa Optical Dissolved Oxygen sensor
GPS, Iridium and Freewave Antennae in tail fin
Webb Slocum Electric Glider
7 ft long
100 lbs in air

## Slide 4
Shelf Glider Sections
~20 km day (21+ day endurance)
Very high spatial resolution
Surface to Bottom coverage (200 m max)
Surface every 1-6 hr to get GPS fix, download data and receive new instructions (via Iridium)
Keep track via web:
gliderfs2.coas.oregonstate.edu/gliderweb
Salinity
T (°C)
Chlorophyll (μg/L)
Backscatter (1/m)
Dissolved Oxygen (mL/L)
May 05 – 10, 2006

## Slide 5
Glider Bob
Glider Jane
Five Seagliders: sg130, sg157, sg158, sg205 & sg206
Bob Smith
Jane Huyer
The OSU Glider Fleet
3 TWR Slocum 200 m
  CTD, chl, bs, cdom, DO
  CTD, microstructure
1 TWR Slocum 1000 m
  CTD, chl, dye, bs, ADCP
5 UW/iRobot/Kongsberg Seagliders 1000 m
  CTD, chl, bs, cdom, DO, PAR

## Slide 6
Not true!
Just because it says autonomous, doesn’t mean you get to sit around and do nothing …

## Slide 7
All platforms have strengths and weaknesses
Glider strengths are low cost, high resolution and long endurance
Glider weaknesses are slow speeds, coarse navigation, and limited payloads
Useful Glider Ops Versus Less-Useful Glider Ops
$$$$
$$$
$$
$$$
$
$$$$
What we must avoid at all costs is the op where you deploy a glider and then follow it around with a research vessel …

## Slide 8
Newport Line
  80 km cross-shelf
  Strong currents (50+ cm/s)
  Complex Bathymetry
  Historical Observations (1950s)
Endurance
April 2006 – Nov 2014
  3486 glider-days at sea
  187 deployments
  82,120 km
  260,190 vertical profiles
Bob
Jane
Seaglider
46050
NWPO3
NH-10
Use a variety of ships to get the gliders in/out of the water
Be prepared for emergency recoveries
Don’t assume piloting will be trivial

## Slide 9
(m/s)
(m)
N-S Wind Speed
Significant Wave Height
2006
2007
2008
2009
2010
2011
2012
December 2007 Storm
35+ ft seas
80 mph winds

## Slide 10
Glider Stories: Jane is in a bit of a pickle …
Wow!!! You are the best glider pilots in the world!!! I bow to your precision!!! osc
Oscar Schofield, Rutgers U.

## Slide 11
We’re collaborating with local fishermen …

## Slide 13
Enhancing Ship-based Survey Footprint
Notes: Additional realizations of SI. Winds begin down-front (SI favorable) but later switch to have a larger cross-front component.

## Slide 14: Average section
Log10 ε (W/kg)
Salinity
Temperature (°C)
Vastly increased data and resolution at the front
Better characterization of the structure on small scales
26.0
25.8
26.0
25.8
26.0
25.8
Notes: Glider observations bin averaged in the cross front direction, using observations from all four gliders

## Slide 15: Continuous Sampling in Bad Weather
Tropical Storm Hanna Sep 2008

## Slide 16: Autono-my-ass
Autonomous Underwater Gliders
  Slow, rough navigation & limited sensor payload
  Cheap, high spatial resolution & long endurance
Useful glider operations
  Endurance, Footprint & Weather